## Slide 1: Stochastic generator for flexible residential load profiles
Context
This work proposes a tool to generate synthetic electrical load profiles using a stochastic occupancy generator[1].
The profiles are designed to include flexibility on the demand side for residential users.
Thomas Stegen*1, Joakim Castiaux1, Noé Diffels1, Maxime Duchesne1, Bertrand Cornélusse1
Profile construction
Each load profile is constructed cumulatively depending on the appliance inside the home.
Result
Conclusion
This tool provides an efficient solution to assess the flexibility of the electrical demand of residential users.
It could be useful to measure efficiency of new tariffication schemes or to quantify potential impact of residential flexibility in the evolution of the load in distribution networks
Reference
[1] Baetens, R., Saelens, D.: ‘Modelling uncertainty in district energy simulations by stochastic residential occupant behaviour’, Journal of Building Performance Simulation, 2016, 9, (4), pp. 431–447
Github of the tool https://github.com/Diffels/ResFlexLoad
1 University of Liège, Montefiore Institute, Liège, Belgium *Corresponding Author: tstegen@uliege.be
Aggregating
All the non-controllable appliances are probabilistically activated.
Base profile
For the whole population, compute yearly profiles to match the predefined probability of the case study
Generate
profiles
To model longer term scenarios, the population characteristics can be updated to account for new usages
Update population
Types and proportions for:
Houses
Families
Cars (+ usage)
Heating systems
Define population
Shiftable controllable loads (washing machine, drier and dishwasher).
Wet appliances
When the car owner leaves home, a “driving event” can start.
Electric vehicle
The hot water needs are converted to electrical consumption.
Water boiler
There are 3 temperature setpoints, wall types and home sizes are modelled.
Space heater
Flexibility
A flexibility component is added to the profiles for each flexible appliance stating when the appliance can or has to be activated.
Different flexibility types can be defined:
Maximum time shift or number of cycles for wet appliances.
Maximum temperature gradient for boilers and HP.
Maximum charging delay for the EVs.