## Slide 1
CIRED 2025 – Paper No: 1092
Introduction
Modelling evolving residential load is key to achieve efficient energy transition and distribution system planning
Conclusions
This tool provides load profiles with a flexibility component that are realistic regarding users’ behavior, assets’ models and populations’ metrics. Results have been validated on Belgian data.
Reference
[1] Baetens, R., Saelens, D.: ‘Modelling uncertainty in district energy simulations by stochastic residential occupant behaviour’, Journal of Building Performance Simulation, 2016
Download the tool https://github.com/Diffels/ResFlex
Occupancy Profile
Using StROBe [1], a family is modelled for the house and their behavior is defined for the full year (Active-Sleeping-Away).
Base Load
Stochastic use of plugged-in appliances is defined depending on presence in house, with data coming from [1].
White Goods
Dishwashers, washing machines and driers with given programs and profiles are launched at specific times.
Water Boiler
A model of water consumption and heating, with thermostatic control is included.
Space Heating
The house is modelled as a block with thermal losses and coefficient. Wall are modelled as a thermal buffer/capacitance.
Electric Vehicle
Driving events with realistic energy use are inferred from the home occupancy profile. Home or outside charge are possible.
Profile generator
The lack of existing public data pushed us to develop synthetic profiles. Our aim is to model known populations from realistic individuals.
Generating a population
This tool aims to model complete distribution grids. Adapted function and inputs can be used to match known parameters for the population from feeder level.
Scenario modelling
For long term planning, evolving populations can be created with increasing penetration parameters representing evolution of the electrification.
1092 – ResFlex: A residential load profile generator to model individual demand response in distribution grids
Thomas Stegen, Joakim Castiaux, Noé Diffels, Maxime Duchesne, Bertrand Cornélusse Montefiore Institute, University of Liège, Belgium

## Slide 2
CIRED 2025 – Paper No: 1092
Introduction
Modelling evolving residential load is key to achieve efficient energy transition and distribution system planning
Conclusions
This tool provides load profiles with a flexibility component that are realistic regarding users’ behavior, assets’ models and populations’ metrics. Results have been validated on Belgian data.
Reference
[1] Baetens, R., Saelens, D.: ‘Modelling uncertainty in district energy simulations by stochastic residential occupant behaviour’, Journal of Building Performance Simulation, 2016
Download the tool https://github.com/Diffels/ResFlex
Profile generator
The lack of existing public data pushed us to develop synthetic profiles. Our aim is to model known populations from realistic individuals.
Generating a population
This tool aims to model complete distribution grids. Adapted function and inputs can be used to match known parameters for the population from feeder level.
Scenario modelling
For long term planning, evolving populations can be created with increasing penetration parameters representing evolution of the electrification.
1092 – ResFlex: A residential load profile generator to model individual demand response in distribution grids
Thomas Stegen, Joakim Castiaux, Noé Diffels, Maxime Duchesne, Bertrand Cornélusse Montefiore Institute, University of Liège, Belgium

## Slide 3
CIRED 2025 – Paper No: 1092
Introduction
Modelling evolving residential load is key to achieve efficient energy transition and distribution system planning
Conclusions
This tool provides load profiles with a flexibility component that are realistic regarding users’ behavior, assets’ models and populations’ metrics. Results have been validated on Belgian data.
Reference
[1] Baetens, R., Saelens, D.: ‘Modelling uncertainty in district energy simulations by stochastic residential occupant behaviour’, Journal of Building Performance Simulation, 2016
Download the tool https://github.com/Diffels/ResFlex
Household Occupancy Profile Generated using StROBe [1]
A family is modelled in the house and individual behavior is defined for the full year (Active-Sleeping-Away).
Profile generator
The lack of existing public data pushed us to develop synthetic profiles. Our aim is to model known populations from realistic individuals.
Generating a population
This tool aims to model complete distribution grids. Adapted function and inputs can be used to match known parameters for the population at feeder level.
Scenario modelling
For long term planning, evolving populations can be created with increasing penetration parameters representing evolution of the electrification.
Thomas Stegen, Joakim Castiaux, Noé Diffels, Maxime Duchesne, Bertrand Cornélusse Montefiore Institute, University of Liège, Belgium
Stochastic use of plugged-in loads
Inhabitants number, types
Activated by people in patterns
No flexibility
Launched at specific times
Cycles per week Program types
Activated for a full cycle
Flexibility windows
Water cons. with thermostat. control
Inhabitants number Boiler model
Hot water usage events
Minimum output T°
Block model with therm. loss & coef.
House year, volume Heating system
Thermostat with three T° setpoints
Thermal comfort
Driving events, energy & charge
Consumption, Max power, km/year
Main driver is back with discharged EV
When plugged
Electric Vehicle
White Goods
Water Boiler
Base Load
Space Heating
1092 – ResFlex: A residential load profile generator to model individual demand response in distribution grids
Complete profile with flexibility component
This tool aims to model complete distribution grids. Adapted function and inputs can be used to match known parameters for the population at feeder level.

## Slide 4
Introduction
Modelling evolving residential load to achieve efficient energy transition and distribution system planning.
Conclusions
This tool provides load profiles with a flexibility component that are realistic regarding users’ behavior, assets’ models and populations’ metrics. Results have been validated on Belgian data.
Reference
[1] Baetens, R., Saelens, D.: ‘Modelling uncertainty in district energy simulations by stochastic residential occupant behaviour’, Journal of Building Performance Simulation, 2016
Download the tool https://github.com/Diffels/ResFlex
Household Occupancy
A family is modelled in the house and individual behavior is defined for the full year using StROBE [1].
Profile generator
Due to lack of data, our aim is to get synthetic profiles for known populations from realistic individuals.
Population
This tool aims to model complete distribution grids. Adapted function and inputs can be used to match known parameters for the population at feeder level.
Scenarios
For long term planning, evolving populations can be created with increasing penetration parameters representing evolution of the electrification.
Thomas Stegen, Joakim Castiaux, Noé Diffels, Maxime Duchesne, Bertrand Cornélusse Montefiore Institute, University of Liège, Belgium
Stochastic use of plugged-in loads
Inhabitants number and occupations
Activated by people in patterns
No flexibility
Launched at specific times
Cycles per week Program types
Activated for a full cycle
Flexibility windows
Water cons. with thermostat. control
Inhabitants number Boiler model
Hot water usage events
Minimum output T°
White Goods
Water Boiler
Base Load
1092 – ResFlex: A residential load profile generator to model individual demand response in distribution grids
Driving events, energy & charge
Consumption, Max power, km/year
Main driver is back with discharged EV
When plugged
Electric Vehicle
Block model with therm. loss & coef.
House year, volume Heating system
Thermostat with three T° setpoints
Thermal comfort
Space Heating
CIRED 2025 – Paper No: 1092
The project source of the results presented in this paper has received funding from the Belgian Energy Transition Fund (UNLEASH Project)

## Slide 5
Goal
Modelling evolving residential load to achieve efficient energy transition and distribution system planning.
Conclusions
This tool provides load profiles with a flexibility component that are realistic regarding users’ behavior, assets’ models and populations’ metrics. Results have been validated on Belgian data.
Reference
[1] Baetens, R., Saelens, D.: ‘Modelling uncertainty in district energy simulations by stochastic residential occupant behaviour’, Journal of Building Performance Simulation, 2016
Download the tool https://github.com/Diffels/ResFlex
Household Occupancy
A family is modelled in the house and individual behavior is defined for the full year using StROBE [1].
Generator
Due to lack of data, our aim is to get synthetic profiles for known populations from realistic individuals.
Population
This tool aims to model complete distribution grids. Adapted function and inputs can be used to match known parameters for the population at feeder level.
Scenarios
For long term planning, evolving populations can be created with increasing penetration parameters representing mass electrification.
Thomas Stegen, Joakim Castiaux, Noé Diffels, Maxime Duchesne, Bertrand Cornélusse Montefiore Institute, University of Liège, Belgium
Stochastic use of plugged-in loads
Inhabitants number and occupations
Activated by people in patterns
No flexibility
Launched at specific times
Cycles per week Program types
Activated for a full cycle
Flexibility windows
Water cons. with thermostat. control
Inhabitants number Boiler model
Hot water usage events
Minimum output T°
White Goods
Water Boiler
Base Load
1092 – ResFlex: A residential load profile generator to model individual demand response in distribution grids
Driving events, energy & charge
Consumption, Max power, km/year
Main driver is back with discharged EV
When plugged
Electric Vehicle
Block model with therm. loss & coef.
House year, volume Heating system
Thermostat with three T° setpoints
Thermal comfort
Space Heating
CIRED 2025 – Paper No: 1092
The project source of the results presented in this paper has received funding from the Belgian Energy Transition Fund (UNLEASH Project)

## Slide 6
Conclusions
This tool provides load profiles with a flexibility component that are realistic regarding users’ behavior, assets’ models and populations’ metrics. Results have been validated on Belgian data.
Reference
[1] Baetens, R., Saelens, D.: ‘Modelling uncertainty in district energy simulations by stochastic residential occupant behaviour’, Journal of Building Performance Simulation, 2016
Download the tool https://github.com/Diffels/ResFlex
Household Occupancy
A family is modelled in the house and individual behavior is defined for the full year using StROBe [1].
Population modelling
This tool aims to model complete distribution grids. Adapted function and inputs can be used to match known parameters for the population at feeder level.
Evolving scenarios
For long term planning, evolving populations can be created with increasing penetration parameters representing mass electrification.
Thomas Stegen, Joakim Castiaux, Noé Diffels, Maxime Duchesne, Bertrand Cornélusse Montefiore Institute, University of Liège, Belgium
Stochastic use of plugged-in loads
Inhabitants number and occupations
Activated by people in patterns
No flexibility
Launched at specific times
Cycles per week Program types
Activated for a full cycle
Flexibility windows
White Goods
Base Load
1092 – ResFlex: A residential load profile generator to model individual demand response in distribution grids
Driving events, energy & charge
Consumption, Max power, km/year
Main driver is back with discharged EV
When plugged
Space Heating
CIRED 2025 – Paper No: 1092
The project source of the results presented in this paper has received funding from the Belgian Energy Transition Fund (UNLEASH Project)
Synthetic generator
Due to lack of data, our aim is to get synthetic profiles for known populations from realistic individuals.
Goal
Modelling evolving residential load to achieve efficient energy transition and distribution system planning.
Water cons. with thermostat. control
Inhabitants number Boiler model
Thermostat with water usage events
Minimum output T°
Electric Vehicle
Block model with therm. loss & coef.
House year, volume Heating system
Thermostat with three T° setpoints
Thermal comfort
Water Boiler

## Slide 7
Conclusions
This tool provides load profiles with a flexibility component that are realistic regarding users’ behavior, assets’ models and populations’ metrics. Results have been validated on Belgian data.
Reference
[1] Baetens, R., Saelens, D.: ‘Modelling uncertainty in district energy simulations by stochastic residential occupant behaviour’, Journal of Building Performance Simulation, 2016
Download the tool https://github.com/Diffels/ResFlex
Household Occupancy
A family is modelled in the house and individual behavior is defined for the full year using StROBe [1].
Population modelling
This tool aims to model complete distribution grids. Adapted function and inputs can be used to match known parameters for the population at feeder level.
Evolving scenarios
For long term planning, evolving populations can be created with increasing penetration parameters representing mass electrification.
Thomas Stegen, Joakim Castiaux, Noé Diffels, Maxime Duchesne, Bertrand Cornélusse Montefiore Institute, University of Liège, Belgium
Launched at specific times
Cycles per week Program types
Activated for a full cycle
Flexibility windows
White Goods
1092 – ResFlex: A residential load profile generator to model individual demand response in distribution grids
Driving events, energy & charge
Consumption, Max power, km/year
Main driver is back with discharged EV
When plugged
Space Heating
CIRED 2025 – Paper No: 1092
The project source of the results presented in this paper has received funding from the Belgian Energy Transition Fund (UNLEASH Project)
Synthetic generator
Due to lack of data, our aim is to get synthetic profiles for known populations from realistic individuals.
Goal
Modelling evolving residential load to achieve efficient energy transition and distribution system planning.
Water cons. with thermostat. control
Inhabitants number Boiler model
Thermostat with water usage events
Minimum output T°
Electric Vehicle
Block model with therm. loss & coef.
House year, volume Heating system
Thermostat with three T° setpoints
Thermal comfort
Water Boiler
Stochastic use of plugged-in loads
Inhabitants number and occupations
Activated by people in patterns
No flexibility
Base Load

## Slide 8
Thomas Stegen, Joakim Castiaux, Noé Diffels, Maxime Duchesne, Bertrand Cornélusse Montefiore Institute, University of Liège, Belgium
1092 – ResFlex: A residential load profile generator to model individual demand response in distribution grids
CIRED 2025 – Paper No: 1092
The project source of the results presented in this paper has received funding from the Belgian Energy Transition Fund (UNLEASH Project)
Household Occupancy
A family is modelled in the house and individual behavior is defined for the full year using StROBe [1].
Reference
[1] Baetens, R., Saelens, D.: ‘Modelling uncertainty in district energy simulations by stochastic residential occupant behaviour’, Journal of Building Performance Simulation, 2016
Download the tool https://github.com/Diffels/ResFlex
Population modelling
This tool aims to model complete distribution grids. Adapted function and inputs can be used to match known parameters for the population at feeder level.
Conclusions
This tool provides load profiles with a flexibility component that are realistic regarding users’ behavior, assets’ models and populations’ metrics. Results have been validated on Belgian data.
Evolving scenarios
For long term planning, evolving populations can be created with increasing penetration parameters representing mass electrification.
Synthetic generator
Due to lack of data, our aim is to get synthetic profiles for known populations from realistic individuals.
Goal
Modelling evolving residential load to achieve efficient energy transition and distribution system planning.
Stochastic use of plugged-in loads
Inhabitants number and occupations
Activated by people in patterns
No flexibility
Base Load
Launched at specific times
Cycles per week Program types
Activated for a full cycle
Flexibility windows
White Goods
Driving events, energy & charge
Consumption, Max power, km/year
Main driver is back with discharged EV
When plugged
Electric Vehicle
Water cons. with thermostat. control
Inhabitants number Boiler model
Thermostat with water usage events
Minimum output T°
Water Boiler
Space Heating
Block model with therm. loss & coef.
House year, volume Heating system
Thermostat with three T° setpoints
Thermal comfort

## Slide 9
CIRED 2025 – Paper No: 1092
Introduction
Modelling evolving residential load is key to achieve efficient energy transition and distribution system planning
Conclusions
This tool provides load profiles with a flexibility component that are realistic regarding users’ behavior, assets’ models and populations’ metrics. Results have been validated on Belgian data.
Reference
[1] Baetens, R., Saelens, D.: ‘Modelling uncertainty in district energy simulations by stochastic residential occupant behaviour’, Journal of Building Performance Simulation, 2016
Download the tool https://github.com/Diffels/ResFlex
Household Occupancy Profile Generated using StROBe [1]
A family is modelled in the house and individual behavior is defined for the full year (Active-Sleeping-Away).
Profile generator
The lack of existing public data pushed us to develop synthetic profiles. Our aim is to model known populations from realistic individuals.
Generating a population
This tool aims to model complete distribution grids. Adapted function and inputs can be used to match known parameters for the population at feeder level.
Scenario modelling
For long-term planning, evolving populations can be created with increasing penetration parameters representing evolution of the electrification.
1092 – ResFlex: A residential load profile generator to model individual demand response in distribution grids
Thomas Stegen, Joakim Castiaux, Noé Diffels, Maxime Duchesne, Bertrand Cornélusse Montefiore Institute, University of Liège, Belgium
Driving events, energy & charge
Consumption, Max power, km/year
Main driver is back with discharged EV
When the car is plugged
Electric Vehicle
Launched at specific times
Cycles per week Program types
Activated for a full cycle
Flexibility windows
White Goods
Water cons. with thermostat. control
Inhabitants number Boiler model
Hot water usage events
Minimum output T°
Water Boiler
Stochastic use of plugged-in loads
Inhabitants number, types
Activated by people in patterns
No flexibility
Base Load
Block model with therm. loss & coef.
House year, volume Heating system
Thermostat with three T° setpoints
Thermal comfort
Space Heating
Description
Parameters
Activation
Flexibility
Complete load profile
A).